## Slide 1: SMART INDIA HACKATHON 2026
VISTRA
Problem Statement ID – 26126
Problem Statement Title- Vision Based Autonomous Navigation for Unmanned Ground Vehicle for Outdoor Environment
Theme- Smart Automation
PS Category- Software
Team ID- 142936
Team Name - NEXORAS

## Slide 2
VISTRA
VISION-BASED AUTONOMOUS NAVIGATION
Camera-first • GPS-denied • Risk-aware • Explainable
❖ PROPOSED SOLUTION
From pixels → confidence → safe driving
VISTRA carries uncertainty from the camera to the wheel commands — then slows, recovers, replans or stops.
HOW VISTRA THINKS
01
CAMERA
RGB / Stereo
02
PERCEPTION
SegFormer-B0
03
RISK MAP
BEV + Entropy
04
LOCALIZATION
VO + EKF
05
PLANNING
D* Lite + DWA
06
SAFETY
TTC + FSM
07
DRIVE
(v,w) → L / R
CONFIDENCE ENGINE
NCS = weakest link
RECOVERY MANAGER
Slow → Stop → Recover → Replan
HOW IT ADDRESSES THE PROBLEM
01
UNKNOWN HAZARDS
Uncertain terrain becomes risky by default. This helps cover ditches, mud and unseen obstacles.
02
VISION DEGRADES
VO + EKF track confidence. Blur, darkness and feature loss trigger controlled recovery.
03
COLLISION RISK
TTC predicts the vehicle for 3 s and checks stopping time against terrain and obstacle risk.
3 CORE INNOVATIONS
UNCERTAINTY → RISK
Entropy + temporal fusion + pose uncertainty
CONFIDENCE → ACTION
Weakest-link NCS controls speed + recovery
TTC → SAFE STOP
Trajectory + stopping time + terrain risk
@SIH Idea submission- NEXORAS
2
NEXORAS

## Slide 3
NEXORAS
TECHNICAL APPROACH
@SIH Idea submission- NEXORAS
3
TECHNOLOGIES
1
AI / COMPUTER VISION
Python • PyTorch • OpenCV • ONNX Runtime
2
PERCEPTION
SegFormer-B0 + YOLOv8n / YOLO11n
3
LOCALIZATION
Stereo VO + EKF • RTAB-Map / ORB-SLAM3
4
PLANNING & SAFETY
D* Lite • DWA • TTC safety layer
5
ROBOTICS
ROS 2 Jazzy • Gazebo Harmonic
6
DASHBOARD
FastAPI + WebSocket • React + TypeScript
IMPLEMENTATION METHODOLOGY
Simulate → perceive → map → localize → plan → verify → benchmark
PROCESS FLOW ARCHITECTURE
1
CAMERA
RGB / stereo
2
PERCEPTION
terrain + objects
3
RISK MAP
BEV + uncertainty
4
LOCALIZE
VO + EKF
GLOBAL PLANNER
D* Lite • A → B
LOCAL PLANNER
DWA • trajectory
SAFETY LAYER
TTC • 3 s prediction
DRIVE
v,w
CONFIDENCE ENGINE
NCS = weakest link
Low confidence → slow / recover / replan / stop
EXPLAINABILITY
Dashboard shows:
risk map • path • NCS • TTC wheel commands • decision reason
PROTOTYPE
Browser-based simulation MVP
Same core software: SIM • VIDEO • WEBCAM • UGV
IMPLEMENTATION
1. Sim world → 2. Perception → 3. Risk + localization → 4. Planning + TTC → 5. Benchmark

## Slide 4
FEASIBILITY AND VIABILITY
Feasibility of VISTRA
Potential Challenges & Risks
LIGHTWEIGHT AI
SegFormer-B0 + ONNX Runtime for efficient terrain segmentation.
GPS-DENIED VO
Stereo VO + EKF bridges visual dropouts and provides pose confidence.
REALISTIC VALIDATION
Gazebo closed-loop tests plus real outdoor video and seeded scenarios.
SAFE NAVIGATION
D* Lite + DWA + TTC layer converts risk into safe motion.
RISK-AWARE MAP
BEV map fuses traversability, uncertainty and pose covariance.
SLAM integration may consume time
Sim-to-real perception gap
Ditch / negative- obstacle recall
High end-to-end latency can affect TTC
Scope creep and metric overfitting
Strategies to Overcome Challenges
Time-box SLAM; keep OpenCV + EKF fallback
Fine-tune on sim + real-video validation
Use uncertainty + geometry to raise risk
Measure latency; include it in stopping time
Freeze scope; seeded tests + held-out sets
Evidence: baseline comparison • seeded scenarios • ablations • FPS/latency • recovery metrics
@SIH Idea submission- NEXORAS
5
NEXORAS

## Slide 5
IMPACT AND BENEFITS
Benefits of VISTRA
✓
✓
✓
✓
V
Safer Navigation
Risk-aware planning and TTC safety reduce collision exposure.
Robust Autonomy
Confidence-gated behavior slows, recovers and safe-stops when uncertain.
Explainable Decisions
Dashboard shows risk, confidence, state changes and replan events.
Practical Validation
Seeded simulation, real outdoor video and baseline comparison support evidence.
Target Users / Stakeholders
•
UGV Operators
•
Autonomy Developers
•
Safety & Validation
•
R&D / Simulation
•
System Integrators
Benefits of the Solution
Chart: 
| Safety | Reliability | Transparency
VISTRA | 1 | 1 | 1
VISTRA
Safety
TTC-based predictive collision avoidance and safe-stop behavior.
Reliability
Confidence engine, recovery manager and pose-aware risk inflation.
Transparency
Live dashboard explains risk, confidence, replans and wheel commands.
6
@SIH Idea submission- NEXORAS
NEXORAS

## Slide 6
RESEARCH AND REFERENCES
• Details Links of the reference and research work
VERIFIED SOURCES USED BY VISTRA
1. SegFormer
Xie et al. (2021) | Semantic segmentation backbone
https://arxiv.org/abs/2105.15203
2. ORB-SLAM3
Campos et al. (2020) | Visual / visual-inertial SLAM
https://arxiv.org/abs/2007.11898
3. D* Lite
Koenig & Likhachev (2002) | Incremental global replanning
https://ocs.aaai.org/Library/AAAI/2002/aaai02-072.php
4. Dynamic Window Approach
Fox, Burgard & Thrun (1997) | Local collision avoidance
https://publications.ri.cmu.edu/the-dynamic-window-approach-to-collision-avoidance
5. RUGD Dataset
Wigness et al. (IROS 2019) | Unstructured outdoor driving data
https://rugd.vision/pdfs/RUGD_IROS2019.pdf
6. RELLIS-3D
Jiang et al. | Multi-modal off-road robotics dataset
https://github.com/unmannedlab/RELLIS-3D
7. ROS 2 Jazzy
Open Robotics | Robotics middleware and integration
https://docs.ros.org/en/jazzy/
8. Gazebo Harmonic
Open Robotics | Closed-loop UGV simulation
https://gazebosim.org/docs/harmonic/getstarted/
9. ONNX Runtime
Microsoft | Model inference/deployment runtime
https://onnxruntime.ai/docs/
@SIH Idea submission- NEXORAS
6
NEXORAS
MVP link: https://vistara-blue.vercel.app/
github Repo link : https://github.com/Zerovion/SIH_26126
Additional Reference Link