## Slide 1: SMART INDIA HACKATHON 2026
PRAGYA-Nav
Problem Statement ID – 26126
Problem Statement Title- Vision Based Autonomous Navigation for Unmanned Ground Vehicle for Outdoor Environment
Theme- Smart Automation
PS Category- Software
Team ID- 142936
Team Name – NEXORAS

## Slide 2: VISTRA: SAFER UGV NAVIGATION
NEXORAS
SIH26126 | Vision-based, GPS-denied, terrain-aware outdoor UGV autonomy
WHY NORMAL NAVIGATION FAILS
1
GPS unavailable
Position must come from vision + motion
2
Unknown, uneven terrain
A detector sees a rock, not whether loose soil is driveable
3
Uncertain vision
Light, shadow, rain and vibration degrade camera cues
4
Shortest path can be unsafe
Mud, ditch, water-like patch, wheel slip
OUR KEY IDEA
The UGV combines what it SEES with what it FEELS while driving.
wheel slip
vibration
motor effort
odometry error
Result: the UGV selects the safest feasible route, not only the shortest route.
Same terrain, two decisions
START
GOAL
mud: high slip risk
water-like?
low confidence
Grass
Soil
Gravel
Mud
Water-like?
Rock
Shortest path (unsafe)
PRAGYA safest path
Typical approach
“Obstacle detected → turn”
PRAGYA-Nav
“Is this terrain safe for my vehicle?”
Terrain
Traversability
Confidence
Grass
HIGH
HIGH
Mud
LOW
HIGH
Unknown
UNKNOWN
LOW
PROPOSED SOLUTION
Camera-based terrain AI classifies soil, grass, gravel, mud and unknown patches
Risk combines terrain, vision uncertainty and pose quality.
Planner picks the safest feasible route and reroutes live
Runs fully offline; no GPS needed
INNOVATION & UNIQUENESS
Learns from physical driving experience (proposed approach)
Confidence gate: unsure → slow or stop
Risk-aware costmap, not just obstacles
Explainable: shows why it slowed or rerouted

## Slide 3: TECHNICAL APPROACH
NEXORAS
Closed loop: SEE → LOCATE → ASSESS → PLAN → ACT → LEARN
1 SEE
Camera
terrain segmentation + obstacle detection
2 LOCATE
Visual-inertial localization
VIO / SLAM + wheel odometry
3 ASSESS
Risk + confidence
for each ground patch → risk-aware costmap
4 PLAN
Safest route
D Lite replans routes. DWA selects local motion.*
5 ACT
Motor control
Confidence + TTC checks before every command
6 LEARN
Vehicle feedback
slip, vibration, motor effort, odometry mismatch
learned terrain experience feeds back into ASSESS
WHAT IT SEES + WHAT IT FEELS
SEES
Camera → terrain + obstacle information
+
FEELS
IMU · wheel odometry · motor effort · slip · vibration
Terrain experience → Risk + Confidence
Planning
SELF-SUPERVISED TERRAIN EXPERIENCE
1
See terrain
2
Drive
3
Observe vehicle response: slip, vibration, motor effort
4
Update terrain risk
5
Store experience
6
Use in future planning
Proposed approach · learns how terrain behaves under its own motion
CONFIDENCE GATE
LOW CONFIDENCE
SLOW DOWN
RE-OBSERVE
REPLAN
SAFE ACTION
Glare, shadow or rain lowers confidence
PLANNED TECH STACK
Python · OpenCV
Small segmentation + detection model
ONNX / TensorRT
Visual-inertial + wheel odometry
A* / D* Lite · ROS 2 Nav2
Jetson / Pi · IMU · encoders

## Slide 4: FEASIBILITY AND VIABILITY
NEXORAS
A focused MVP that we can build, test and demonstrate
WHAT WE WILL BUILD (MVP)
MUST HAVE
Terrain segmentation
Obstacle / person detection
VIO + wheel odometry
Risk costmap + D* Lite
Dynamic rerouting
Slip / vibration risk score
Safe stop + dashboard
SHOULD HAVE
Terrain memory
Confidence visualization
Live dashboard with reason for slow / reroute / stop
FUTURE
Advanced self-supervised learning
Thermal / radar fallback
Multi-UGV shared maps
Large-scale deployment
PROTOTYPE HARDWARE (PROPOSED)
Stereo / RGB camera
primary vision
IMU + encoders
motion feedback
Jetson / Pi edge computer
ROS 2 · AI + localization · Nav2 planner
Motor driver + E-stop → UGV
SAFETY SUPERVISOR
NORMAL
Normal speed
LOW CONFIDENCE
Slow + re-observe
HIGH RISK
Crawl + replan
CRITICAL
Controlled stop
RECOVERY
Relocalize / return / operator help
MAIN RISK → OUR MITIGATION
Glare / shadows
Use confidence score; slow, crawl or stop
SLAM tracking loss
Relocalize; use IMU + encoders; last-safe-point recovery
Unknown terrain
Mark as high risk; never enter blindly
Slow compute
Small model + ONNX / TensorRT optimization
BUILD ROADMAP
1 Perception
2 Localization
3 Planning
4 Terrain learning
5 Field test
Safe-response triggers: SLAM lost · human detected · ditch · high slip · low confidence
DEMO FLOW
illustrative scenario
01
Normal terrain
02
Obstacle / risky terrain appears
03
Perception identifies terrain
04
Risk score changes
05
Planner picks safer route
06
UGV moves
07
Vehicle feedback updates terrain experience

## Slide 5: IMPACT AND BENEFITS
NEXORAS
Why PRAGYA-Nav matters beyond the SIH demo
WHERE IT HELPS
Search & Rescue
Floods, forest, rubble, low visibility
Defence Logistics
GPS-denied, communication-limited terrain
Agriculture
Uneven soil, crop rows, irrigation channels
Industrial Inspection
Mines, solar farms, construction sites
Expected benefits to validate
Safety: avoids uncertain or high-slip terrain
Reliability: GPS-free local navigation and rerouting
Adaptability: learns terrain behaviour for this vehicle
Explainability: dashboard states why it slowed or rerouted
Scalability: works offline; reusable on many UGV platforms
TYPICAL VISION-ONLY UGV vs PRAGYA-Nav (PROPOSED)
Feature
Illustrative baseline
PRAGYA-Nav
GPS dependency
Often GPS / map assisted
Designed for GPS-denied operation
Terrain awareness
Obstacle level
Terrain class + risk per patch
Risk estimation
Distance / obstacle cost
Terrain risk inside the costmap
Confidence estimation
Usually not used
Per-patch confidence gate
Vehicle feedback
Odometry for pose
Slip, vibration, motor effort
Dynamic rerouting
Obstacle-driven
Risk-driven
Learning from driving
Typically none
Terrain experience (proposed)
Safe-stop mechanism
E-stop / bumper stop
Supervisor: slow, crawl, controlled stop
Uncertainty handling
Limited
Slows, re-observes, replans
Offline / edge capability
Varies
Edge compute, fully offline
Qualitative design comparison by our team; to be validated with field-test data.
FUTURE SCOPE: Thermal / radar fallback · Multi-UGV shared terrain maps · Active learning from field data
Mission outcome: safer autonomous movement where maps, GPS and predictable roads cannot be assumed.

## Slide 6: RESEARCH AND REFERENCES
NEXORAS
Why our solution is technically grounded
EXISTING RESEARCH WE BUILD ON
1
Official SIH26126 Problem Statement
GPS-denied outdoor UGV: safe path / hazard detection, visual localization, dynamic rerouting
Used for:
Problem scope
2
TerraPN (arXiv:2202.12873)
Learns surface properties such as traction and bumpiness from robot–terrain interaction
Used for:
Physical terrain feedback
3
WayFAST (IEEE 2022) / WayFASTER (arXiv:2402.00683)
Self-supervised traversability prediction for off-road mobile robots
Used for:
Visual traversability
4
Visual SLAM research reviews
Need for robust fusion and uncertainty awareness in real outdoor conditions
Used for:
Localization + uncertainty
5
ROS 2 Nav2 / open-source robotics stack
Practical costmap, planner, controller and modular deployment foundation
Used for:
Planning + deployment
OUR PROPOSED INTEGRATION
What it SEES
visual traversability
(WayFAST, WayFASTER)
What it FEELS
terrain interaction
(TerraPN)
PRAGYA-Nav
Camera-based terrain prediction is calibrated by the UGV’s own physical experience, then used for confidence-aware safe planning.
Proposed integration of existing ideas; not a validated result yet.
Our contribution: a practical closed loop of visual terrain prediction + physical experience + confidence-aware safe planning.
Source links: sih2026.vuce.in/ps/SIH26126 | arxiv.org/abs/2202.12873 | arxiv.org/abs/2402.00683 | IEEE WayFAST | ROS 2 Nav2