## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID –
Problem Statement Title-
Theme-
PS Category- Software/Hardware
Team ID-
Team Name (Registered on portal)

## Slide 2: PRAGYA-Nav: SAFER UGV NAVIGATION
PRAGYA-Nav
SIH26126 | Vision-based, GPS-denied, terrain-aware outdoor UGV autonomy
WHY NORMAL NAVIGATION FAILS
1
GPS unavailable
Position must come from vision + motion
2
Unknown, uneven terrain
A detector sees a rock, not whether loose soil is driveable
3
Uncertain vision
Light, shadow, rain and vibration degrade camera cues
4
Shortest path can be unsafe
Mud, ditch, water-like patch, wheel slip
OUR KEY IDEA
The UGV combines what it SEES with what it FEELS while driving.
wheel slip
vibration
motor effort
odometry error
Result: the UGV selects the safest feasible route, not only the shortest route.
Same terrain, two decisions
START
GOAL
mud: high slip risk
water-like?
low confidence
Grass
Soil
Gravel
Mud
Water-like?
Rock
Shortest path (unsafe)
PRAGYA safest path
Typical approach
“Obstacle detected → turn”
PRAGYA-Nav
“Is this terrain safe for my vehicle?”
Terrain
Traversability
Confidence
Grass
HIGH
HIGH
Mud
LOW
HIGH
Unknown
UNKNOWN
LOW
PROPOSED SOLUTION
Camera-based terrain AI classifies soil, grass, gravel, mud and unknown patches
Every patch gets a risk score and a confidence value
Planner picks the safest feasible route and reroutes live
Runs fully offline; no GPS needed
INNOVATION & UNIQUENESS
Learns from physical driving experience (proposed approach)
Confidence gate: unsure → slow or stop
Risk-aware costmap, not just obstacles
Explainable: shows why it slowed or rerouted

## Slide 3: TECHNICAL APPROACH
PRAGYA-Nav
Closed loop: SEE → LOCATE → ASSESS → PLAN → ACT → LEARN
1 SEE
Camera
terrain segmentation + obstacle detection
2 LOCATE
Visual-inertial localization
VIO / SLAM + wheel odometry
3 ASSESS
Risk + confidence
for each ground patch → risk-aware costmap
4 PLAN
Safest route
A* / D* Lite on the costmap, live rerouting
5 ACT
Motor control
safety check before every command
6 LEARN
Vehicle feedback
slip, vibration, motor effort, odometry mismatch
learned terrain experience feeds back into ASSESS
WHAT IT SEES + WHAT IT FEELS
SEES
Camera → terrain + obstacle information
+
FEELS
IMU · wheel odometry · motor effort · slip · vibration
Terrain experience → Risk + Confidence
Planning
SELF-SUPERVISED TERRAIN EXPERIENCE
1
See terrain
2
Drive
3
Observe vehicle response: slip, vibration, motor effort
4
Update terrain risk
5
Store experience
6
Use in future planning
Proposed approach · learns how terrain behaves under its own motion
CONFIDENCE GATE
LOW CONFIDENCE
SLOW DOWN
RE-OBSERVE
REPLAN
SAFE ACTION
Glare, shadow or rain lowers confidence
PLANNED TECH STACK
Python · OpenCV
Small segmentation + detection model
ONNX / TensorRT
Visual-inertial + wheel odometry
A* / D* Lite · ROS 2 Nav2
Jetson / Pi · IMU · encoders

## Slide 4: FEASIBILITY AND VIABILITY
PRAGYA-Nav
A focused MVP that we can build, test and demonstrate
WHAT WE WILL BUILD (MVP)
MUST HAVE
Terrain segmentation
Obstacle / person detection
VIO + wheel odometry
Risk costmap + D* Lite
Dynamic rerouting
Slip / vibration risk score
Safe stop + dashboard
SHOULD HAVE
Terrain memory
Confidence visualization
Live dashboard with reason for slow / reroute / stop
FUTURE
Advanced self-supervised learning
Thermal / radar fallback
Multi-UGV shared maps
Large-scale deployment
PROTOTYPE HARDWARE (PROPOSED)
Stereo / RGB camera
primary vision
IMU + encoders
motion feedback
Jetson / Pi edge computer
ROS 2 · AI + localization · Nav2 planner
Motor driver + E-stop → UGV
SAFETY SUPERVISOR
NORMAL
Normal speed
LOW CONFIDENCE
Slow + re-observe
HIGH RISK
Crawl + replan
CRITICAL
Controlled stop
RECOVERY
Relocalize / return / operator help
MAIN RISK → OUR MITIGATION
Glare / shadows
Use confidence score; slow, crawl or stop
SLAM tracking loss
Relocalize; use IMU + encoders; last-safe-point recovery
Unknown terrain
Mark as high risk; never enter blindly
Slow compute
Small model + ONNX / TensorRT optimization
BUILD ROADMAP
1 Perception
2 Localization
3 Planning
4 Terrain learning
5 Field test
Safe-response triggers: SLAM lost · human detected · ditch · high slip · low confidence
DEMO FLOW
illustrative scenario
01
Normal terrain
02
Obstacle / risky terrain appears
03
Perception identifies terrain
04
Risk score changes
05
Planner picks safer route
06
UGV moves
07
Vehicle feedback updates terrain experience

## Slide 5: IMPACT AND BENEFITS
PRAGYA-Nav
Why PRAGYA-Nav matters beyond the SIH demo
WHERE IT HELPS
Search & Rescue
Floods, forest, rubble, low visibility
Defence Logistics
GPS-denied, communication-limited terrain
Agriculture
Uneven soil, crop rows, irrigation channels
Industrial Inspection
Mines, solar farms, construction sites
BENEFITS WE CAN PROVE IN FIELD TESTING
Safety: avoids uncertain or high-slip terrain
Reliability: GPS-free local navigation and rerouting
Adaptability: learns terrain behaviour for this vehicle
Explainability: dashboard states why it slowed or rerouted
Scalability: works offline; reusable on many UGV platforms
TYPICAL VISION-ONLY UGV vs PRAGYA-Nav (PROPOSED)
Feature
Typical vision-only UGV
PRAGYA-Nav
GPS dependency
Often GPS / map assisted
Designed for GPS-denied operation
Terrain awareness
Obstacle level
Terrain class + risk per patch
Risk estimation
Distance / obstacle cost
Terrain risk inside the costmap
Confidence estimation
Usually not used
Per-patch confidence gate
Vehicle feedback
Odometry for pose
Slip, vibration, motor effort
Dynamic rerouting
Obstacle-driven
Risk-driven
Learning from driving
Typically none
Terrain experience (proposed)
Safe-stop mechanism
E-stop / bumper stop
Supervisor: slow, crawl, controlled stop
Uncertainty handling
Limited
Slows, re-observes, replans
Offline / edge capability
Varies
Edge compute, fully offline
Qualitative design comparison by our team; to be validated with field-test data.
FUTURE SCOPE: Thermal / radar fallback · Multi-UGV shared terrain maps · Active learning from field data
Mission outcome: safer autonomous movement where maps, GPS and predictable roads cannot be assumed.

## Slide 6: RESEARCH AND REFERENCES
PRAGYA-Nav
Why our solution is technically grounded
EXISTING RESEARCH WE BUILD ON
1
Official SIH26126 Problem Statement
GPS-denied outdoor UGV: safe path / hazard detection, visual localization, dynamic rerouting
Used for:
Problem scope
2
TerraPN (arXiv:2202.12873)
Learns surface properties such as traction and bumpiness from robot–terrain interaction
Used for:
Physical terrain feedback
3
WayFAST (IEEE 2022) / WayFASTER (arXiv:2402.00683)
Self-supervised traversability prediction for off-road mobile robots
Used for:
Visual traversability
4
Visual SLAM research reviews
Need for robust fusion and uncertainty awareness in real outdoor conditions
Used for:
Localization + uncertainty
5
ROS 2 Nav2 / open-source robotics stack
Practical costmap, planner, controller and modular deployment foundation
Used for:
Planning + deployment
OUR PROPOSED INTEGRATION
What it SEES
visual traversability
(WayFAST, WayFASTER)
What it FEELS
terrain interaction
(TerraPN)
PRAGYA-Nav
Camera-based terrain prediction is calibrated by the UGV’s own physical experience, then used for confidence-aware safe planning.
Proposed integration of existing ideas; not a validated result yet.
Our contribution: a practical closed loop of visual terrain prediction + physical experience + confidence-aware safe planning.
Source links: sih2026.vuce.in/ps/SIH26126 | arxiv.org/abs/2202.12873 | arxiv.org/abs/2402.00683 | IEEE WayFAST | ROS 2 Nav2