## Slide 1
VISTRA | SIH PS 26126 | Detailed evidence pack
VISTRA
Vision-based, Self-aware, Traversability- and Risk-aware Autonomy
PS 26126
Vision-based autonomous navigation for an outdoor UGV
CORE THESIS
Uncertainty from perception -> risk -> planner -> behavior
EVIDENCE
Seeded simulation + baseline + fault injection + replay
SOURCE INTEGRITY
PS-specific content: supplied VISTRA blueprint. External facts: trusted source register. No unmeasured performance claims.

## Slide 2
VISTRA | SIH PS 26126 | Detailed evidence pack
1 | Problem & solution
Target: explainable, uncertainty-aware outdoor navigation
PS REQUIREMENTS
Lightweight perception Visual odometry / SLAM Planning + wheel/motor commands Collision-free A -> B
CONVENTIONAL GAP
Detector-only perception can miss untrained hazards Hard binary maps hide model uncertainty
VISTRA RESPONSE
Free-space-first risk map NCS behavior gate TTC safety override
EVIDENCE LOOP
Baseline vs VISTRA on identical seeds; fault injection for blur/dark/obstacle; structured logs; measured FPS/latency; scenario-level statistics
IMPORTANT
This deck contains no fabricated VISTRA performance numbers.

## Slide 3
VISTRA | SIH PS 26126 | Detailed evidence pack
2 | Architecture
Camera-first closed loop
1. PERCEPTION
Camera SegFormer-B0 Dynamic-object tracking Input quality
2. MAP
IPM Traversability Entropy BEV risk + fusion
3. LOCALIZE
Stereo VO/SLAM EKF Pose + covariance
4. PLAN
D* Lite DWA Goal + risk + clearance
5. SAFETY
TTC NCS Recovery Wheels
FEEDBACK LOOPS
Pose covariance inflates risk-map costs; NCS caps speed; localization failure invokes Recovery Manager; planning failure escalates to replan / rotate-search / safe stop
DASHBOARD
Camera overlay | BEV map | pose/path | NCS | TTC | state/e-stop | structured explanation | replan markers | wheel commands | fault injection | baseline comparison

## Slide 4
VISTRA | SIH PS 26126 | Detailed evidence pack
3 | Risk-aware traversability
Probabilities are retained instead of collapsed to one class
CORE FORMULAE
T = sum(p_k * t_k) U = normalized entropy(p) R = (1-T) + lambda_u U + lambda_g G + lambda_prox P
BEV
Example: 20 m x 20 m at 0.2 m = 100 x 100 cells Temporal log-odds / decay
6 CLASSES
Smooth-drivable; Rough-drivable; Vegetation/non-traversable; Hard obstacle; Water/ditch/negative; Background/sky
RISK BANDS
Green <0.25 Yellow <0.5 Orange <0.75 Red >=0.75 or lethal
LIMITATION
IPM assumes locally flat ground. Proposed mitigation: IMU pitch/roll compensation and lower weight for far-range cells.
SegFormer paper
SegFormer docs

## Slide 5
VISTRA | SIH PS 26126 | Detailed evidence pack
4 | Localization & recovery
Stereo vision remains primary; degraded states are explicit
PRIMARY PATH
Stereo VO/SLAM + loop-closure RTAB-Map or ORB-SLAM3 IMU/wheel EKF bridges short gaps
CONFIDENCE SIGNALS
Features; RANSAC inliers; reprojection error; EKF covariance; blur; brightness; feature distribution
NORMAL
>0.7 nominal speed cap
CAUTION
0.4-0.7 slow + inflate
RECOVER
0.2-0.4 relocalize/re-observe
SAFE_STOP
<0.2 hold + alert
RECOVERY SEQUENCE
confidence fall -> slow -> stop -> rotate-search -> retrace to last good keyframe -> resume after confidence restoration
ORB-SLAM3 paper
ROS 2 Jazzy

## Slide 6
VISTRA | SIH PS 26126 | Detailed evidence pack
5 | Planning + predictive safety
Global route, local motion and a reactive override
GLOBAL
D* Lite Incremental replanning on risk grid
LOCAL
DWA Reachable (v,w) progress + risk + clearance
TTC
3 s horizon 0.1 s steps constant-velocity obstacle model
STOPPING TIME
tau_stop = t_latency + v/a_max Latency is measured end-to-end. Planner mapping: v_left = v - wL/2 v_right = v + wL/2
STARTING TTC RULES
>3*tau_stop: continue 1.5*tau_stop-3*tau_stop: slow + replan tau_stop-1.5*tau_stop: hard brake + replan <=tau_stop: emergency stop
D* Lite
DWA
Gazebo Harmonic

## Slide 7
VISTRA | SIH PS 26126 | Detailed evidence pack
6 | Data & datasets
Public data for research; held-out real data for validation
RUGD
7,453 pixel-wise labeled images Unstructured outdoor robot driving Irregular boundaries + blur challenges
RELLIS-3D
13,556 LiDAR scans 6,235 images 20-class ontology Multimodal off-road data
SEGFORMER-B0
MiT-B0: 3.7M parameters in HF docs Project FPS must be measured
TRAIN / VALIDATE
Sequence/location-level splits Held-out real set never used in training Hard negatives: shadows, puddles, grass hiding rocks, glare
PROJECT DATA
Blueprint plans about 300-500 campus/trail frames This is a plan, not a completed result.
INTEGRITY
Never import paper metrics into VISTRA result tables.
RUGD
RELLIS-3D
ONNX Runtime

## Slide 8
VISTRA | SIH PS 26126 | Detailed evidence pack
7 | Benchmark protocol
Evidence comes from repeated seeded experiments
SCENARIOS
11 families: terrain, obstacles, lighting, localization, perception, narrow paths, dead ends, route choice, unknown obstacles
RUNS
20-30 seeded runs per scenario per system Mean + confidence interval
BASELINE
YOLOv8 + same VO/SLAM + A* + fixed-distance stop
METRICS
Success; collisions; path length; time; localization error; path deviation; replans; FPS; latency; NCS trace; recovery time
ABLATIONS
A: remove uncertainty term B: remove confidence governor C: remove TTC/terrain safety
RULE
If the baseline wins a scenario, report it. Do not fabricate or hide results.

## Slide 9
VISTRA | SIH PS 26126 | Detailed evidence pack
8 | Dashboard & explainability
The system should show not just what it does, but why
PERCEPTION VIEW
Camera feed + segmentation overlay
MAP VIEW
BEV risk map + global/local path + actual path + pose
SAFETY VIEW
NCS + components + TTC + speed + state/e-stop
EXPLANATION FEED
time | state | trigger | confidence | speed cap | chosen action
INTERACTION
Spawn obstacle; blur; darken; camera loss; baseline comparison; replan markers
DATA FLOW
FastAPI/WebSocket -> React/TypeScript -> 2D canvas/SVG. Offline starter included in Source-Code/Dashboard.
FastAPI
CVAT

## Slide 10
VISTRA | SIH PS 26126 | Detailed evidence pack
9 | Risks, limits and roadmap
Build the core first; protect the benchmark
HIGH RISKS
SLAM integration time Sim-to-real gap Ditch recall Latency too high for TTC Scope creep
MITIGATIONS
Time-box SLAM Separate real-video track Uncertainty + geometry Measure end-to-end latency Freeze scope
MUST-HAVE
Simulation + vehicle interface Segmentation + BEV risk VO + EKF D* Lite + DWA TTC + dashboard + benchmark
IMPORTANT
NCS Recovery Manager Decision log Fault injector
ADVANCED / OPTIONAL
Relative depth Moving-object prediction Live side-by-side Physical UGV after core
ROADMAP
Weeks 1-6: build and freeze core. Weeks 7-10: test, benchmark and rehearse.
Gazebo Harmonic official docs

## Slide 11
VISTRA | SIH PS 26126 | Detailed evidence pack
10 | Judge-ready demo
A simple, observable sequence
01
No GPS Empty map
02
Segmentation Risk map builds
03
Drive A -> B Path visible
04
Obstacle fault TTC + replan
05
Blur/dark NCS drops
06
Recover Relocalize
07
Reach goal Metrics summary
08
Baseline Same seed
BACKUP
Rosbag replay; pre-rendered full run; recorded-video perception; playback dashboard
SOURCE
B1

## Slide 12
11 | Trusted sources
Click a source label to open the official page or paper
S1 | BEL official
OPEN
S2 | ROS 2 Jazzy
OPEN
S3 | Gazebo Harmonic
OPEN
S4 | SegFormer paper
OPEN
S5 | SegFormer docs
OPEN
S6 | ORB-SLAM3 paper
OPEN
S7 | D* Lite
OPEN
S8 | DWA
OPEN
S9 | RUGD paper
OPEN
S10 | RELLIS-3D repo
OPEN
S11 | RELLIS-3D paper
OPEN
S12 | ONNX Runtime
OPEN
S13 | CVAT
OPEN
S14 | OpenCV
OPEN
S15 | FastAPI
OPEN
PS-specific VISTRA details: supplied blueprint. External facts: source register. Research date: 30 Sep 2026.